## Slide 1: Digital Circuit Experiment Time Sequence Circuit with Asynchronous Counter
Lecture 5
Rencan Nie（聂仁灿）

## Slide 2: Theoretical Basis
Asynchronous Counter
The term asynchronous refers to events that do not have a fixed time relationship with each other and, generally, do not occur at the same time. An asynchronous counter is one in which the flip-flops (FF) within the counter do not change states at exactly the same time because they do not have a common clock pulse.

## Slide 3: Theoretical Basis
Asynchronous Counter
Asynchronous Binary Up Counter
Each FF in a binary up counter must satisfies with two conditions:
The next state of the FF will be changed, when a counting pulse appears.
The FF must output a carry bit to another FF.
CP |  | Equivalent decimal number
0 | 0 0 | 0
1 | 0 1 | 1
2 | 1 0 | 2
3 | 1 1 | 3
CP |  | Equivalent decimal number
0 | 0 0 | 0
1 | 0 1 | 1
2 | 1 0 | 2
3 | 1 1 | 3
0 + 1 = 1
1 + 1 =1 0
Toggle !

## Slide 4: Theoretical Basis
Asynchronous Counter
Asynchronous Binary down Counter
Each FF in a binary down counter must satisfies with two conditions:
The next state of the FF will be changed, when a counting pulse appears.
The FF must output a borrow bit to another FF.
CP |  | Equivalent decimal number
0 | 1 1 | 3
1 | 1 0 | 2
2 | 0 1 | 1
3 | 0 0 | 0
CP |  | Equivalent decimal number
0 | 1 1 | 3
1 | 1 0 | 2
2 | 0 1 | 1
3 | 0 0 | 0
10 - 1 = 1
1 - 1 = 0
Toggle !

## Slide 5: Theoretical Basis
Asynchronous Counter
Basic Counter Unit with FF
A counter can be designed using a D-FF or JK-FF, where a FF must have the function of toggle.
Toggle !

## Slide 6: Theoretical Basis
Asynchronous Counter
Basic Counter Unit with FF
A counter can be designed using a D-FF or JK-FF, where a FF must have the function of toggle.
Toggle !

## Slide 7: Theoretical Basis
Asynchronous Counter
A 2-Bit Asynchronous Binary Counter
A 2-bit counter connected for asynchronous operation as follows.
Notice that the clock (CLK) is applied to the clock input (C) of only the first flip-flop, FF0, which is always the least significant bit (LSB). The second flip-flop, FF1, is triggered by the Q0 output of FF0. FF0 changes state at the positive-going edge of each clock pulse, but FF1 changes only when triggered by a positive-going transition of the Q0 output of FF0.

## Slide 8: Theoretical Basis
Asynchronous Counter
A 3-Bit Asynchronous Binary Counter
A 4-bit counter connected for asynchronous operation as follows.

## Slide 9: Experiments
Experimental purposes
  Test the function of a 4-bit asynchronous binary up counter designed by JK-FF.
  Understand how to design and test a 4-bit asynchronous binary up counter using JK-FF.
  Understand how to design and test a 3-bit asynchronous binary up counter using D-FF.
  Understand how to design and test a 3-bit asynchronous binary down counter using D-FF.

## Slide 10
Task 1. Test an asynchronous binary up counter
Step 1: Design an 4-bit asynchronous binary Up Counter with JK flip-flop
Experimental Contents
There are four JK-FF in two 74LS112 chips

## Slide 11
Task 1. Test an asynchronous binary up counter
Step 2: Design the circuit in Quartus 13.1
Experimental Contents
CP | Q3Q2Q1Q0
0 | 0 0 0 0
1 | 0 0 0 1
2 | 0 0 1 0
3 | 0 0 1 1
4 | 0 1 0 0
5 | 0 1 0 1
6 | 0 1 1 0
7 | 0 1 1 1
8 | 1 0 0 0
9 | 1 0 0 1
10 | 1 0 1 0
11 | 1 0 1 1
12 | 1 1 0 0
13 | 1 1 0 1
14 | 1 1 1 0
15 | 1 1 1 1

## Slide 12
Task 1. Test an asynchronous binary up counter
Step 3: Compile the designed file, and construct the VMF to watch the simulation results about Q3Q2Q1Q0
Experimental Contents
This counter also is a frequency divider!

## Slide 13
Task 2. Design and Test an asynchronous binary down counter
Principles:
Experimental Contents
That means that the low FF will output a significant bit to the high FF, when =1
CP |  | Equivalent decimal number
0 | 1 1 | 3
1 | 1 0 | 2
2 | 0 1 | 1
3 | 0 0 | 0
CP |  | Equivalent decimal number
0 | 1 1 | 3
1 | 1 0 | 2
2 | 0 1 | 1
3 | 0 0 | 0
10 - 1 = 1
1 - 1 = 0
Toggle !
The FF used has the function of toggle.
The FF must output a borrow bit to another FF.

## Slide 14
Task 2. Design and Test an asynchronous binary down counter
The circuit designed:
Experimental Contents
The low FF will output a significant bit to the high FF, when =1
CP |  | Equivalent decimal number
0 | 1 1 | 3
1 | 1 0 | 2
2 | 0 1 | 1
3 | 0 0 | 0
CP |  | Equivalent decimal number
0 | 1 1 | 3
1 | 1 0 | 2
2 | 0 1 | 1
3 | 0 0 | 0
10 - 1 = 1
1 - 1 = 0
Toggle !

## Slide 15
Task 2. Design and Test an asynchronous binary down counter
The simulation results:
Experimental Contents
The low FF will output a significant bit to the high FF, when =1
CP |  | Equivalent decimal number
0 | 1 1 | 3
1 | 1 0 | 2
2 | 0 1 | 1
3 | 0 0 | 0
CP |  | Equivalent decimal number
0 | 1 1 | 3
1 | 1 0 | 2
2 | 0 1 | 1
3 | 0 0 | 0
10 - 1 = 1
1 - 1 = 0
Toggle !

## Slide 16
Task 3. Design and Test an 3-bit asynchronous binary up counter using D-FF
Experimental Contents
CP |  | Equivalent decimal number
0 | 0 0 0 | 0
1 | 0 0 1 | 1
2 | 0 1 0 | 2
3 | 0 1 1 | 3
4 | 1 0 0 | 4
5 | 1 0 1 | 5
6 | 1 1 0 | 6
7 | 1 1 1 | 7
CP |  | Equivalent decimal number
0 | 0 0 0 | 0
1 | 0 0 1 | 1
2 | 0 1 0 | 2
3 | 0 1 1 | 3
4 | 1 0 0 | 4
5 | 1 0 1 | 5
6 | 1 1 0 | 6
7 | 1 1 1 | 7
Toggle !
0 + 1 = 1
1 + 1 =1 0
74LS74!

## Slide 17
Task 4. Design and Test an 3-bit asynchronous binary down counter using D-FF
Experimental Contents
10 - 1 = 1
1 - 1 = 0
Toggle !
CP |  | Equivalent decimal number
0 | 0 0 0 | 7
1 | 0 0 1 | 6
2 | 0 1 0 | 5
3 | 0 1 1 | 4
4 | 1 0 0 | 3
5 | 1 0 1 | 2
6 | 1 1 0 | 1
7 | 1 1 1 | 0
CP |  | Equivalent decimal number
0 | 0 0 0 | 7
1 | 0 0 1 | 6
2 | 0 1 0 | 5
3 | 0 1 1 | 4
4 | 1 0 0 | 3
5 | 1 0 1 | 2
6 | 1 1 0 | 1
7 | 1 1 1 | 0
74LS74!

## Slide 18: Thanks