## Slide 1: Digital Circuit Experiment Asynchronous Integrated Counter
Lecture 6
Rencan Nie（聂仁灿）

## Slide 2: Theoretical Basis
Counter
Modulus
The modulus of a counter is the number of unique states through which the counter will sequence. For a counter with flip-flops:
Maximum modulus: Possible outputs:
Counters can be designed to have a number of states in their sequence that is less than the maximum of . This type of sequenceis called a truncated sequence.

## Slide 3: Theoretical Basis
Counter
Partial Decoding
Notice in Following that only and are connected to the NAND gate inputs. This arrangement is an example of partial decoding, in which the two unique states ( = 1 and = 1) are sufficient to decode the count of ten because none of the other states (0 through 9) have both and HIGH at the same time. When the counter goes into count ten (1010), the decoding gate output goes LOW and asynchronously resets all the flip-flops as 0.
CP | Q3Q2Q1Q0
0 | 0 0 0 0
1 | 0 0 0 1
2 | 0 0 1 0
3 | 0 0 1 1
4 | 0 1 0 0
5 | 0 1 0 1
6 | 0 1 1 0
7 | 0 1 1 1
8 | 1 0 0 0
9 | 1 0 0 1
10 | 1 0 1 0
11 | 1 0 1 1
12 | 1 1 0 0
13 | 1 1 0 1
14 | 1 1 1 0
15 | 1 1 1 1

## Slide 4: Theoretical Basis
Counter
Partial Decoding: CLR based method
CP | Q3Q2Q1Q0
0 | 0 0 0 0
1 | 0 0 0 1
2 | 0 0 1 0
3 | 0 0 1 1
4 | 0 1 0 0
5 | 0 1 0 1
6 | 0 1 1 0
7 | 0 1 1 1
8 | 1 0 0 0
9 | 1 0 0 1
10 | 1 0 1 0
11 | 1 0 1 1
12 | 1 1 0 0
13 | 1 1 0 1
14 | 1 1 1 0
15 | 1 1 1 1
If , the first way to make the counter recycle after the count of is to decode count with a logical gate and connect the output of the logical gate to the clear (CLR) inputs of the flip-flops. CLR port will reset the output of the counter as 0.
0：0000
1：0001
2：0010
3：0011
4：0100
5：0101
6：0000
7：0110
15：1111
14：1110
13：1101
12：1100
11：1011
10：1001
9：1001
8：1000
Recycle with M = 10 states
transient state

## Slide 5: Theoretical Basis
Counter
Partial Decoding: CLR based method
CP | Q3Q2Q1Q0
0 | 0 0 0 0
1 | 0 0 0 1
2 | 0 0 1 0
3 | 0 0 1 1
4 | 0 1 0 0
5 | 0 1 0 1
6 | 0 1 1 0
7 | 0 1 1 1
8 | 1 0 0 0
9 | 1 0 0 1
10 | 1 0 1 0
11 | 1 0 1 1
12 | 1 1 0 0
13 | 1 1 0 1
14 | 1 1 1 0
15 | 1 1 1 1
Example 1:
pls design 11 modulus asynchronous counter using JK-FF, employing CLR based method
Step 1: give the state transition diagram
0：0000
1：0001
2：0010
3：0011
4：0100
5：0101
6：0000
7：0110
11：1011
10：1001
9：1001
8：1000
Recycle with M = 11 states
transient state

## Slide 6: Theoretical Basis
Counter
Partial Decoding: CLR based method
CP | Q3Q2Q1Q0
0 | 0 0 0 0
1 | 0 0 0 1
2 | 0 0 1 0
3 | 0 0 1 1
4 | 0 1 0 0
5 | 0 1 0 1
6 | 0 1 1 0
7 | 0 1 1 1
8 | 1 0 0 0
9 | 1 0 0 1
10 | 1 0 1 0
11 | 1 0 1 1
12 | 1 1 0 0
13 | 1 1 0 1
14 | 1 1 1 0
15 | 1 1 1 1
Example: pls design 11 asynchronous modulus counter using JK-FF, employing CLR based method
Step 2: design the circuit expected
The logical gate is designed based on the transient state
The logical gate is connected with CLR

## Slide 7: Theoretical Basis
Counter
Partial Decoding: CLR based method
CP | Q3Q2Q1Q0
0 | 0 0 0 0
1 | 0 0 0 1
2 | 0 0 1 0
3 | 0 0 1 1
4 | 0 1 0 0
5 | 0 1 0 1
6 | 0 1 1 0
7 | 0 1 1 1
8 | 1 0 0 0
9 | 1 0 0 1
10 | 1 0 1 0
11 | 1 0 1 1
12 | 1 1 0 0
13 | 1 1 0 1
14 | 1 1 1 0
15 | 1 1 1 1
Example 1: pls design 11 modulus asynchronous counter using JK-FF, employing CLR based method
Step 3: Simulation results
11

## Slide 8: Theoretical Basis
Counter
Partial Decoding: LD based method
CP | Q3Q2Q1Q0
0 | 0 0 0 0
1 | 0 0 0 1
2 | 0 0 1 0
3 | 0 0 1 1
4 | 0 1 0 0
5 | 0 1 0 1
6 | 0 1 1 0
7 | 0 1 1 1
8 | 1 0 0 0
9 | 1 0 0 1
10 | 1 0 1 0
11 | 1 0 1 1
12 | 1 1 0 0
13 | 1 1 0 1
14 | 1 1 1 0
15 | 1 1 1 1
If , and the counter want to count starting from 0, the way to make the counter recycle after the count of +N-1 through a load data (LD) port. LD port will reset the output of the counter as a number with N.
0：0000
1：0001
2：0010
3：0011
4：0100
5：0101
6：0000
7：0110
15：1111
14：1110
13：1101
12：1100
11：1011
10：1001
9：1001
8：1000
Recycle with M =10 states
Counting N=3 through 12

## Slide 9: Theoretical Basis
Integrated Asynchronous Counter
74LS90
74LS290 is a integrated asynchronous counter.
Contain two counters
A: output QA (2 modulus)
B: output QD QC QB (5 modulus)
CLK ports:
CLKA: the clock of A counter
CLKB: the clock of B counter
CLR ports:
If CLRA = CLRA=1, QD QC QB QA = 0 0 0 0
Setting 9 ports:
If SET9A = SET9B=1, QD QC QB QA = 1 0 0 1

## Slide 10: Theoretical Basis
Integrated Asynchronous Counter
How to Design a asynchronous counter using 74LS90
Example 2: Pls design a counter with 10 modulus
Tips:
A 74LS290 just has maximal modulus with 2X5=10
A Cascaded counter using two counters A and B
Disable CLR and SET9 ports

## Slide 11: Theoretical Basis
Integrated Asynchronous Counter
How to Design a asynchronous counter using 74LS90
Example 3: Pls design a counter with 7 modulus
Tips:
Design a 10 modulus counter firstly
Enable CLR, when Q3Q2Q1Q0=7 (0111)
Disable SET9 ports

## Slide 12: Theoretical Basis
Integrated Asynchronous Counter
How to Design a asynchronous counter using 74LS90
Example 3: Pls design a counter with 7 modulus -----(simulation results)

## Slide 13: Theoretical Basis
Integrated Asynchronous Counter
How to Design a asynchronous counter using 74LS90
Example 4: Pls design a counter with 56 modulus
Tips (method1):
Design a 10x10 modulus counter firstly
Enable CLR, when Q7Q6Q5Q4Q3Q2Q1Q0=56 (00111000), that is Q5Q4Q3=111
Disable SET9 ports

## Slide 14: Theoretical Basis
Integrated Asynchronous Counter
How to Design a asynchronous counter using 74LS90
Example 4: Pls design a counter with 56 modulus
Step1: Design a counter with 100 modulus
method1

## Slide 15: Theoretical Basis
Integrated Asynchronous Counter
How to Design a asynchronous counter using 74LS90
Example 4: Pls design a counter with 56 modulus
Step2: Enable CLR, when Q7Q6Q5Q4Q3Q2Q1Q0=56 (00111000), that is Q5Q4Q3=111
method1

## Slide 16: Theoretical Basis
Integrated Asynchronous Counter
How to Design a asynchronous counter using 74LS90
Example 4: Pls design a counter with 56 modulus
Step3: watch the simulation results
method1

## Slide 17: Theoretical Basis
Integrated Asynchronous Counter
How to Design a asynchronous counter using 74LS90
Example 5: Pls design a counter with 56 modulus
Tips (method2):
Design 7, 8 modulus counter respectively, because 7x8=56
Cascade those of two counters.
Disable SET9 ports in those of two counters

## Slide 18: Theoretical Basis
Integrated Asynchronous Counter
How to Design a asynchronous counter using 74LS90
Example 5: Pls design a counter with 56 modulus
Step1: Design 7, 8 modulus counter respectively
method2
7 modulus
8 modulus

## Slide 19: Theoretical Basis
Integrated Asynchronous Counter
How to Design a asynchronous counter using 74LS90
Example 5: Pls design a counter with 56 modulus
Step2: Cascade those of two counters.
Method 2

## Slide 20: Theoretical Basis
Integrated Asynchronous Counter
How to Design a asynchronous counter using 74LS90
Example 5: Pls design a counter with 56 modulus
Step3: watch the simulation results
method2

## Slide 21: Experiments
Experimental purposes
  Understand how to design and test a M-modules asynchronous counter using JK-FF, resorting to CLR port.
  Based on the total CLR based method, understand how to design and test a M-modules asynchronous counter, through integrated chips.
  Based on the multi-modulus cascade-based method, understand how to design and test a M-modules asynchronous counter, through integrated chins.

## Slide 22
Task 1. Design and test a 13 modules asynchronous counter with JK-FF
Step 1: Design a 13 modules asynchronous counter using JK-FF
Experimental Contents
Pls consult the Example 1!!!
Step 2: input the counting pulses to the designed counter, then test and record the waves for different output bits with Q3~Q0.

## Slide 23
Task 2. Design and test a 6 modules asynchronous counter with 74LS90
Step 1: Design a 6 modules asynchronous counter using 74LS90
Experimental Contents
Pls consult the Example 3!!!
Step 2: input the counting pulses to the designed counter, then test and record the waves for different output bits with Q3~Q0.

## Slide 24
Task 3. Design and test a 69 modules asynchronous counter with 74LS90
Step 1: Design a 69 modules asynchronous counter using 74LS90, based on the total CLR based method.
Experimental Contents
Pls consult the Example 4!!!
Step 2: input the counting pulses to the designed counter, then test and record the waves for different output bits with Q7~Q0.

## Slide 25
Task 3. Design and test a 69 modules asynchronous counter with 74LS90
Step 1: Design a 69 modules asynchronous counter using 74LS90, Based on the multi-modulus cascade-based method, that is 54=6*9.
Experimental Contents
Pls consult the Example 5!!!
Step 2: input the counting pulses to the designed counter, then test and record the waves for different output bits with Q7~Q0.

## Slide 26: Thanks