## Slide 1: Digital Circuit Experiment Design and Test Synchronous Counter
Lecture 7
Rencan Nie（聂仁灿）

## Slide 2: Theoretical Basis
Synchronous Counter
The term synchronous refers to events that have a fixed time relationship with each other. A synchronous counter is one in which all the flip-flops in the counter are clocked at the same time by a common clock pulse. J-K flip-flops are used to illustrate most synchronous counters. D flip-flops can also be used but generally require more logic because of having no direct toggle or no-change states.

## Slide 3: Theoretical Basis
Transition Map
JK-FF
0
1
J=1
K = X
J=X
K = 1
J=0
K = X
J=X
K = 0
X: arbitrary state, i.e. X=0 or 1

## Slide 4: Theoretical Basis
Transition Map
D-FF
0
1
D=1
D=0
D=0
D=1

## Slide 5: Theoretical Basis
Design of Synchronous Counters
Step 1: State Diagram
The first step in the design of a state machine (counter) is to create a state diagram. A state diagram shows the progression of states through which the counter advances when it is clocked. As an example, the following Figure is a state diagram for a basic 3-bit Gray code counter.

## Slide 6: Theoretical Basis
Design of Synchronous Counters
Step 2: Next-State Table
Once the sequential circuit is defined by a state diagram, the second step is to derive a next-state table, which lists each state of the counter (present state) along with the corresponding next state. The next state is the state that the counter goes to from its present state upon application of a clock pulse.

## Slide 7: Theoretical Basis
Design of Synchronous Counters
Step 3: Flip-Flop Transition Table
The following Table is a transition table for the J-K flip-flop. All possible output transitions are listed by showing the Q output of the flip-flop going from present states to next states.
0
1
J=1
K = X
J=X
K = 1
J=0
K = X
J=X
K = 0

## Slide 8: Theoretical Basis
Design of Synchronous Counters
Step 4: Next state Karnaugh Map
The following right Table is a Next state Karnaugh Maps, which is can be derived from the next state. Each cell denote the next state, whereas a output, Q2Q1Q0 , is a certain present state.
 | 0 | 1
00 | 001 | 011
01 | 110 | 010
11 | 111 | 101
10 | 000 | 100
Q2Q1
Q0

## Slide 9: Theoretical Basis
Design of Synchronous Counters
Step 5: Karnaugh Maps
Karnaugh maps can be used to determine the logic required for the J and K inputs of each flip-flop in the counter. There is a Karnaugh map for the J input and a Karnaugh map for the K input of each flip-flop. In this design procedure, each cell in a Karnaugh map represents one of the present states in the counter sequence.
 | 0 | 1
00 | 001 | 011
01 | 110 | 010
11 | 111 | 101
10 | 000 | 100
Q2Q1
Q0

## Slide 10: Theoretical Basis
Design of Synchronous Counters
Step 5: Karnaugh Maps
 | 0 | 1
00 | 001 | 011
01 | 110 | 010
11 | 111 | 101
10 | 000 | 100
Q2Q1
Q0
Karnaugh maps can be used to determine the logic required for the J and K inputs of each flip-flop in the counter. There is a Karnaugh map for the J input and a Karnaugh map for the K input of each flip-flop. In this design procedure, each cell in a Karnaugh map represents one of the present states in the counter sequence.

## Slide 11: Theoretical Basis
Design of Synchronous Counters
Step 5: Karnaugh Maps
 | 0 | 1
00 | 001 | 011
01 | 110 | 010
11 | 111 | 101
10 | 000 | 100
Q2Q1
Q0
Karnaugh maps can be used to determine the logic required for the J and K inputs of each flip-flop in the counter. There is a Karnaugh map for the J input and a Karnaugh map for the K input of each flip-flop. In this design procedure, each cell in a Karnaugh map represents one of the present states in the counter sequence.

## Slide 12: Theoretical Basis
Design of Synchronous Counters
Step 6: Logic Expressions for Flip-Flop Inputs
From the Karnaugh maps we can obtain the following expressions for the J and K inputs of each flip-flop:

## Slide 13: Theoretical Basis
Design of Synchronous Counters
Step 7: Counter Implementation
The final step is to implement the combinational logic from the expressions for the J and K inputs and connect the flip-flops to form the complete 3-bit Gray code counter as following.
XNOR
XOR

## Slide 14: Theoretical Basis
Example
Example 1
There is a Design a irregular binary count sequence 1, 2, 5, 7. Pls design a counter with this count sequence through using D-FF
Step 1: State Diagram
Present the state diagram for this irregular binary count sequence 1, 2, 5 7.
001 (1)
010 (2)
111 (7)
011 (5)

## Slide 15: Theoretical Basis
Example
Example 1
There is a Design a irregular binary count sequence 1, 2, 5, 7. Pls design a counter with this count sequence through using D-FF
Step 2: Next State Table
Present the next state table for this sequence according to its state diagram .
001 (1)
010 (2)
111 (7)
101 (5)
Next State Table |  |  |  |  | 
Present State | Present State |  | Next State |  | 
Q2 | Q1 | Q0 | Q2 | Q1 | Q0
0 | 0 | 1 | 0 | 1 | 0
0 | 1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 0 | 1

## Slide 16: Theoretical Basis
Example
Example 1
There is a Design a irregular binary count sequence 1, 2, 5, 7. Pls design a counter with this count sequence through using D-FF
Step 3: Flip-Flop Transition Table
Present the D-FF Transition Table.
0
1
D=1
D=0
D=0
D=1

## Slide 17: Theoretical Basis
Example
Example 1
There is a Design a irregular binary count sequence 1, 2, 5, 7. Pls design a counter with this count sequence through using D-FF
Step 4: Next state Karnaugh Map
Present the next state Karnaugh map according to next state table .
 | 0 | 1
00 | X | 010
01 | 101 | X
11 | X | 001
10 | X | 111
Q2Q1
Q0
Next State Table |  |  |  |  | 
Present State | Present State |  | Next State |  | 
Q2 | Q1 | Q0 | Q2 | Q1 | Q0
0 | 0 | 1 | 0 | 1 | 0
0 | 1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 0 | 1

## Slide 18: Theoretical Basis
Example
Example 1
There is a Design a irregular binary count sequence 1, 2, 5, 7. Pls design a counter with this count sequence through using D-FF
Step 4: Karnaugh Maps
Present the Karnaugh Maps for each D-FF according to next state Karnaugh map and the D-FF Transition Table.
 | 0 | 1
00 | X | 010
01 | 101 | X
11 | X | 001
10 | X | 111
Q2Q1
Q0
 | 0 | 1
00 | X | 0
01 | 1 | X
11 | X | 1
10 | X | 1
Q2Q1
Q0
D0

## Slide 19: Theoretical Basis
Example
Example 1
There is a Design a irregular binary count sequence 1, 2, 5, 7. Pls design a counter with this count sequence through using D-FF
Step 5: Karnaugh Maps
Present the Karnaugh Maps for each D-FF according to next state Karnaugh map and the D-FF Transition Table.
 | 0 | 1
00 | X | 010
01 | 101 | X
11 | X | 001
10 | X | 111
Q2Q1
Q0
 | 0 | 1
00 | X | 1
01 | 0 | X
11 | X | 0
10 | X | 1
Q2Q1
Q0
D1

## Slide 20: Theoretical Basis
Example
Example 1
There is a Design a irregular binary count sequence 1, 2, 5, 7. Pls design a counter with this count sequence through using D-FF
Step 5: Karnaugh Maps
Present the Karnaugh Maps for each D-FF according to next state Karnaugh map and the D-FF Transition Table.
 | 0 | 1
00 | X | 010
01 | 101 | X
11 | X | 001
10 | X | 111
Q2Q1
Q0
 | 0 | 1
00 | X | 0
01 | 1 | X
11 | X | 0
10 | X | 1
Q2Q1
Q0
J2

## Slide 21: Theoretical Basis
Example
Example 1
There is a Design a irregular binary count sequence 1, 2, 5, 7. Pls design a counter with this count sequence through using D-FF
Step 6: Logic Expressions for Flip-Flop Inputs
Present the logic expressions for D-FF Inputs according to the Karnaugh Maps.
 | 0 | 1
00 | X | 0
01 | 1 | X
11 | X | 1
10 | X | 1
Q2Q1
Q0
D0

## Slide 22: Theoretical Basis
Example
Example 1
There is a Design a irregular binary count sequence 1, 2, 5, 7. Pls design a counter with this count sequence through using D-FF
Step 6: Logic Expressions for Flip-Flop Inputs
Present the logic expressions for D-FF Inputs according to the Karnaugh Maps.
 | 0 | 1
00 | X | 1
01 | 0 | X
11 | X | 0
10 | X | 1
Q2Q1
Q0
D1

## Slide 23: Theoretical Basis
Example
Example 1
There is a Design a irregular binary count sequence 1, 2, 5, 7. Pls design a counter with this count sequence through using D-FF
Step 6: Logic Expressions for Flip-Flop Inputs
Present the logic expressions for D-FF Inputs according to the Karnaugh Maps.
 | 0 | 1
00 | X | 0
01 | 1 | X
11 | X | 0
10 | X | 1
Q2Q1
Q0
J2
+

## Slide 24: Theoretical Basis
Example
Example 1
There is a Design a irregular binary count sequence 1, 2, 5, 7. Pls design a counter with this count sequence through using D-FF
Step 7: Counter Implementation
Design the circuit for this counter according to the Logic Expressions .

## Slide 25: Thanks